## Slide 1: Understanding the Stealthy BGP Hijacking Risks in the ROV Era
Yihao Chen, Qi Li, Ke Xu, Zhuotao Liu, Jianping Wu
Tsinghua University

## Slide 2: Content
BGP Hijacking in the ROV Era: A Real-World Case
Stealthy BGP Hijacking
Empirical Analysis & Insights
Simulation-Based Risk Evaluation
Discussion & Future Work

## Slide 3: BGP Hijacking in the ROV Era: A Real-World Case
AS37100
SEACOM Ltd., MU
AS6762
TISparkle, IT
AS7473
SingTel, SG
AS3758
SingNet Pte Ltd., SG
AS15412
FLAG Telecom, UK
AS4775
Globe Telecoms, PH
AS17894
Innove Comm., PH
To 203.127.0.0/16
To 203.127.225.0/24
ROV
Target
Hijacker?
RPKI: valid
IRR: match
RPKI: invalid
IRR: conflict
* First observed: 2023-10-01 Recently observed: 2025-02-05
* While in the form of BGP hijacking, this case is very likely to be caused by misconfiguration; we awaiting response from relevant operators.
AS17894 mis-announces a /24 without RPKI or IRR authorization, while AS3758 is the legitimate origin
ROV-enabled AS37100 discards the invalid route, and thus has the legitimate /16 route only
   By seeing routing tables, AS37100 and its customers are not aware of the potential hijacking attempt, and tend to believe their traffic be forwarded correctly.
However, legacy AS6762 accepts the illegitimate route, actually forwarding /24 traffic to AS17894
BGP hijacking still succeeds, and becomes less spotted (stealthier), due to the incomplete ROV deployment in the current Internet?

## Slide 4: RPKI/ROV in Today’s Internet
ROAs have covered 53.9% IPv4 prefixes and 59.2% IPv6 prefixes*
Yet ROV deployment is presumably limited
* Source: https://rpki-monitor.antd.nist.gov/ROV
APNIC
RoVista
Cloudflare

## Slide 5: BGP Hijacking Under Partial ROV deployment
B
C
E
A
D
F
G
ROV
ROV
Hijacker
Target
Hijacked traffic
Protected traffic
malicious ann.
benign ann.
Hijacked
Protected
Protected
or Hijacked?
* This is the general topology structure that illustrates how BGP hijacking could succeed despite partial ROV deployment. It does not reflect the whole Inter-AS topology, but only the part that makes the stealthy hijacking scenario possible.
multi-hop
one-hop

## Slide 6: AS A’s Perspective
B
C
E
A
D
F
G
ROV
ROV
Hijacker
Target
Expected traffic propagation
Hijacker invisible (not reachable)
The hijacker is invisible to AS A on the control plane, due to the ROV filtering of AS B
AS A would expect its traffic safely forwarded along the correct path (green)

## Slide 7: Global Perspective
B
C
E
A
D
F
G
ROV
ROV
Hijacker
Target
Actual traffic propagation
(as expected)
Actual traffic propagation (hijacked)
AS C diverts traffic
to the hijacker
AS C, however, is not protected by ROV, and diverts traffic to the hijacker, as long as it accepts the prefix (either the target prefix or a subprefix of it) announced by the hijacker.
AS A falls victim to hijacking unknowingly.

## Slide 8: Stealthy Hijacking: An Unexpected Consequence
BGP hijacking that is invisible from the victim on the control plane
B
C
E
A
D
F
G
ROV
ROV
Hijacker
Target
Hijacked traffic
Protected traffic
Hijacked (stealthy hijacking)
Hijacked (direct hijacking)
Protected
malicious ann.
benign ann.
multi-hop
one-hop

## Slide 9: Empirical Analysis of Stealthy Hijacking in the Wild
Data Sources
  RIB data from RouteViews collectors (route-views2, amsix, wide) on Oct 1, 2023 (56M routes, 86 vantage points).
  Validation: RIPE NCC RPKI, RADB IRR, WHOIS from 5 RIRs, CAIDA AS Organization dataset..
Results
  26 incidents: 19 linked to poor route engineering (e.g., outdated RPKI/IRR), 7 potential hijacks.
  Affected: 1,205 routes, 40 prefixes, 27 origins.
#0 Most wild stealthy hijacking is caused by bad route engineering practice.

## Slide 10: Empirical Analysis: Public Service
* Daily analysis results since 2025-01-01
Our website to publish stealthy hijacking incidents in the wild:
https://yhchen.cn/stealthy-bgp-hijacking/
Set up search options and date range
Search your interested ASN/prefix/organization
Review the results and feedback
Beta feature: GPT analysis with routing knowledge augmentation

## Slide 11: Simulation-Based Risk Evaluation
Questions unanswered:
The prevalence, extent, distribution, influencing factors, etc. of the risk within our real-world Internet.
Is it possible to comprehensively evaluate the stealthy hijacking risk introduced by the current ROV deployment?
Challenges: Criteria to identify risk? Knowledge of routes?
Measurement of ROV deployment? ......
Use CAIDA AS relationships to reconstruct Internet topology
Use APNIC, RoVista, Cloudflare measurement to gain ROV deployment status
Perform BGP simulation on the topology and generate all Internet-scale routes
Thoroughly analyze all possible “victim-target-hijacker” 3-tuple to determine those at risk of stealthy BGP hijacking.

## Slide 12: Results: Overall Risk Level
Stealthy Hijacking | Sub-Prefix | Exact-Prefix
w/ ROV | 0.104 | 0.001
w/o ROV | 0.000 | 0.000
Direct Hijacking | Sub-Prefix | Exact-Prefix
w/ ROV | 0.658 | 0.144
w/o ROV | 0.986 | 0.338
▲0.104
▲0.001
▼0.328
▼0.194
#1 The overall success rate of stealthy hijacking increases from 0 to 10.4%, solely due to the partial ROV deployment in today’s Internet.

## Slide 13: Results: Aggregated Risk Level
#2 Targeted stealthy hijacking has high success rates on specific AS pairs (up to 99.5%), while non-targeted one spreads risk more evenly (within 21.0%).

## Slide 14: Results: Risk Distribution
#3 Stealthy hijacking risks typically follow an opposing trend to direct hijacking as ROV’s impact increases.
#4 Arguably, ASes most capable of hijacking are mainly in Europe and parts of North America. Victim-prone ASes are mainly in North America. Target-prone ASes are mainly in South America and South Asia.

## Slide 15: Results: Influencing Factors
#5 Among different features, cumulative statistics of AS hegemony exhibit highest quadratic correlation with the risk.
#6 A small set of risk-critical and ROV-enabled ASes account for the majority of stealthy hijacking risk.

## Slide 16: Discussion & Future Work
Limitations of the approach
  Prefix-specific routing simulation?
  Accuracy-coverage trade-off of ROV cross validation?
  Complex routing policy?
Potential practical application
  For ISP operation: risk assessment before peering plans
  To defend attacks: targeted probing, analysis with real-world routes, ……
Risk countermeasures
  Keep increasing RPKI/ROV deployment (as indicated in #3)
  Co-analyzing routing data from multiple VP to identify inconsistencies
  Collaboration among ROV-enabled ASes to share threat information
  Active blackholing on detecting stealthy hijacking (like in ROV++)

## Slide 17: Summary
Motivation: a real-world case
Approach: empirical + simulation-based
Evaluation: seven takeaways
Discussion: limitations & future work

## Slide 18
Thank you!
Key Takeaways
Partial ROV deployment introduces stealthy hijacking risks to the current Internet.
Risk evaluation can be achieved with complete knowledge of routes and ROV deployment.
Our approach cross-validates multiple sources of ROV measurements and infers BGP routes.
A 10.4% success rate of stealthy hijacking is introduced by the current ROV deployment.
Contact: yh-chen21@mails.tsinghua.edu.cn (Yihao Chen)
Online Service: https://yhchen.cn/stealthy-bgp-hijacking/
Q&A

## Slide 19: Appendix: Simulation-Based Analysis Workflow
malicious reach
AS Rel.
benign reach
initial states
iterative
matrix update
Matrix-Based BGP Simulation
final states
ROV meas.
benign route set
malicious
route set
Victim
Target
Hijacker
None
C2P
P2P
P2C
ROV
node set
edge set
ROV set
parse
cross
validate
Internet topology
core topology
branch
pruning
ROV
ROV
Topology Construction
benign route set
malicious
route set
Stealthy Hijacking Analysis
one-byte
encoding
route
restore
1
2
3
discover all stealthy hijacking instances
distrib.
corr.
magn.
geoloc.
“victim-target-hijacker” 3-tuples
comprehensive analysis results

## Slide 20: Appendix: Gap in Risk Evaluation
ROV++ [Morillo et al, NDSS’21]
  Assume unrealistic ROV deployment for experiments.
  Evaluate with limited stealthy hijacking samples.
  Present overall hijacking rate only.
Is it possible to comprehensively evaluate the stealthy hijacking risk introduced by the current ROV deployment?
Questions unanswered:
The prevalence, extent, distribution, influencing factors, etc. of the risk within our real-world Internet.
Challenges: Criteria to identify risk? Knowledge of routes?
Measurement of ROV deployment? ......